## Slide 1: Wind Turbine Failure Analysis - Project
EDA Insights Summary

## Slide 2: Failure vs Non-Failure Distribution
#1 — Failures are rare
Most of the records are normal (non-failure).
- So failure is a rare event (imbalanced dataset)

## Slide 3: Gear Oil Temperature vs Failure
Condition | Gear Oil Temp
No Failure | ~15°C
Failure | ~19.6°C
Average Gear Oil Temperature :
→ Big temperature spike before failure → Gearbox lubrication breaking down → mechanical friction increasing

## Slide 4: Generator Bearing Temperature vs Failure
Condition | Bearing Temp
No Failure | ~17.6°C
Failure | ~22.2°C
Average Bearing Temp:
→ Bearings overheating → internal mechanical stress This confirms a consistent thermal pattern.

## Slide 5: Wind Speed vs Power Output
As wind speed rises:
0 – 8 m/s → low power 8 – 20 m/s → power increases sharply ~23 m/s → TURBINE PEAK POWER
25 m/s → power drops again (safety cut-out)
→ This proves the dataset is realistic (this is how real turbines behave)

## Slide 6: Correlation and Feature Insights

## Slide 7: Thermal sensors have the strongest relationship with failure
Sensor | Correlation with Failure
Gear Oil Temp | High
Bearing Temp | High
Wheel Hub Temp | High
Nacelle Temp | Medium
Correlation heatmap showed:
→ Temperature is the best failure predictor
Wind speed / yaw / direction → weak failure link

## Slide 8: Key Insights
Failures are rare in dataset.
Turbine components(Gear Oil & Bearing Temps ) heat up before failing.
Wind vs Power curve realistic: peaks ~23 m/s .
Thermal sensors = strong predictors of failure.